## Slide 1: Two-Way Transit Signal Priority Algorithm for Optimizing Transit Reliability and Speed A Deep Reinforcement Learning Approach
Wen Xun Hu, Chuhan Chen, Hirotaka Ishihara, Islam Taha, Amer Shalaby and Baher Abdulhai
TAL Research Day, July 6th, 2021

## Slide 2: Motivation
The transit reliability and speed are performance indicators
Transit services are vulnerable to variability and delays
No strategies can adaptively improve headway regularity and reduce signal delays simultaneously
The conventional TSP only aims at reducing delays
Multiple TSP requests from different approaches are commonly handled by FCFS logic
Model of the dynamics of transportation environment

## Slide 3: Objectives
Dual-objective TSP
  Adaptively optimize reliability (i.e., headway regularity) and reduce signal delays simultaneously
Coordination of opposite directions
  Develop an algorithm to coordinate TSP in opposite directions of the same intersection based on real-time bus performance

## Slide 4: Objectives
Adaptively optimize reliability (i.e., headway regularity) and
travel time of buses coming from two opposite directions
Headway issue
Delays from traffic light
TRANSIT SIGNAL PRIORITY
Source: Wylie Poon
Source: https://www.thestar.com/news/gta/2020/11/27/the-ttc-wants-to-test-platoons-of-driverless-buses.html
Source: Kevin Van Paassen
Source: Raysonho
Notes: Photo:
Wylie Poon, https://archive.citybuildinginstitute.ca/2019/07/03/we-need-surface-transit-innovations-while-toronto-waits-for-subways/
Kevin Van Paassen, https://www.theglobeandmail.com/news/toronto/ttc-pilot-project-reduces-use-of-streetcar-short-turns/article22000738/
Raysonho, https://www.wikiwand.com/en/Bus_priority_signal; credit: Raysonho @Open Grid Scheduler /Grid Engine; License: Creative Commons Zero, Public Domain Dedication
Focus and objective of study
Objective: Develop a TSP algorithm that adaptively and simultaneously optimize reliability and travel time of buses from two opposite directions
Why do we want to emphasize reliability/headway regularity?
Improving headway regularity and reducing transit delays are both important. Uneven headways, like long headways, result in crowdedness at bus tops; short headways lead to bunching. Passengers travel on bus lines with irregular headways experience excessive waiting time, which is out-of-vehicle travel time.
In-vehicle travel time is increased when there is transit delays, a great portion of which can be attributed to traffic light.
Does there exist a single strategy that can adaptively improve both headway regularity and travel time?
No.
Transit Signal Priority (TSP)
Effective in reducing signal delays
Does not guarantee improvement in reliability

## Slide 5: Model Formulation
One-Way DRL Agent
POZ
Check-out Loop detector
Check-in Loop detector
Model-free deep reinforcement learning
Efficient for large state space

## Slide 6: Model Formulation
One-Way DRL Agent
• Target travel time to maintain scheduled headway at check-out
• Number of vehicles in the POZ
• Time to the end of 1st available green
reward =
Transportation network simulated in Aimsun
TSP control system
Green phase:
-20, -15, -10, -5, 0, +5, +10, +15, +20 sec
Source: Pawel Czerwinski, unsplash.com

## Slide 7: Model Formulation
Coordination Algorithm
RL agent X
Coordination algorithm
RL agent Y

## Slide 8: Simulation case study
Aimsun Next Microsimulation
Intersection in Toronto
Bus line: 36 Finch West
  Traffic during AM peak
  AVL
  Signal timing cards
Finch Ave West at Kipling Ave
Subnetwork

## Slide 9: Results
Base scenarios
  No TSP
  TSP in field (Toronto TSP)
  DRL agents + FCFS logic (FCFS TSP)
Proposed scenario
  DRL agents + coordination algorithm (D2 TSP)
Source: Pawel Czerwinski, unsplash.com
Source: Andre Furtado, unsplash.com

## Slide 10: Results
Coefficient of Variation of Headway
Chart: 
| No TSP | Toronto | FCFS | D2 TSP
EB | 0.46075 | 0.43888 | 0.41655 | 0.40807
WB | 0.50238 | 0.50502 | 0.48226 | 0.45596

## Slide 11: Results
% of Extreme Headways
Chart: 
| h < 0.25 hs | h < 0.5 hs | h > 1.5 hs | h > 1.75 hs
No TSP | 0.033809 | 0.18332 | 0.22089 | 0.083396
Toronto | 0.038346 | 0.16842 | 0.20752 | 0.066917
FCFS | 0.016517 | 0.13889 | 0.16892 | 0.072823
D2 TSP | 0.012003 | 0.13128 | 0.15379 | 0.059265

## Slide 12: Results
Travel Time
Chart: 
| No TSP | Toronto | FCFS | D2 TSP
EB | 90.6872 | 66.3564 | 77.8541 | 73.0947
WB | 91.3289 | 60.1736 | 57.6528 | 62.4889
9 s travel time ↑,
23 s stdev of h dev↓ = 10 s waiting time↓

## Slide 13: Conclusions
The proposed Two-Way TSP (D2 TSP)
Generates the best headway performance in both directions
  Effective in reducing headway variability and % of extreme headways
Brings noticeable reduction in travel time compared with “No TSP”
Source: Kayla Speid, unsplash.com

## Slide 14: Future Work
Coordinated TSP systems to enhance the benefit on transit reliability and speed at the route level
Use connected vehicle technologies for detection and communication
Integrate TSP design with other route strategies
Source: Nong Vang, unsplash.com

## Slide 15: Acknowledgement
Huawei Canada Research Centre

## Slide 16
THANK YOU!
wenxun.hu@mail.utoronto.ca
Source: chuttersnap, unsplash.com